## Slide 1
22. März 2024
A07591000
Bosch Rodez
Assembly Solenoid Armature

## Slide 2
William Bauguil Manufacturing sector (RzP/MFE1)
Tel: +33 5 6567-9485 |
Mobile +33 6 3426-4481 |
Mail: William.Bauguil@fr.bosch.com
contact person at Gluth:
Harald Waas Projektierung / project planning Tel: +49 9421 544-918 Mobile: +49 160 98 363 373
Mail: harald.waas@gluth.de
contact person at BOSCH:
Assembly Solenoid Armature
Contact

## Slide 3
5 kN
±0,025
Feed pin
(tray 300 pcs.
200x400mm)
Feed plate
(bulk - bowl feeder
capacity 300 pcs.)
Press
(Kistler press)
Check
(Heidenhain gauge)
Cycle time: 8,2 sec.
Type 1
Type 2
Type 3
Type 4
1
2
6
7
Assembly Solenoid Armature
Components

## Slide 4
Plate
Bulk - bowl feeder
capacity min. 300 pcs.
Pin
Tray 200x400
capacity 300 pcs.
Palletizer assembled parts
Tray 300x450
capacity 50 pcs.
Palletizer with 2x6 trays
6x full / 6x empty
Press
Check
Cycle time: 8,2 sec.
1
2
6
7
8
5
2400
1400
Feeder Pin
Convoyer forTray 200x400
capacity 300 pcs.
Feeder Plate
bowl feeder
capacity min. 300 pcs.
Handling Plate
Pneumatic axis and gripper
Vibration rail to Kistler press
Handling Pin / Solenoid Armature
Pneumatic pilgrim step hanlding with 3 grippers
Robot handling Pin / Solenoid Armature
Staubli TS2-80 with single pneumatic gripper
Press
Kistler press max. 10kN
Check
Heidenhain gauge
Palletizer assembled parts
Palletizer with 2x6 trays
NIO parts
Drawer with 10 parts
SPC parts
Drawer with 10 parts
10
11
3
4
1
2
3
4
5
6
7
8
10
11
6x loaded
6x empty
processing tray
processing tray
loaded
empty
Assembly Solenoid Armature
Layout

## Slide 5
F = max. 5,5kN
v = 100 ±50 mm/min
Pressing time max. 4 sec.
±0,025
from bowl feeder (handling)
bowl feeder capacity min. 300 pcs.
from tray (robot)
tray 300 pcs. 200x400mm
into tray (robot)
tray 50 pcs. 300x450mm
Press
(Kistler press)
Check
(Heidenhain gauge)
6
7
Cycle time: 8,2 sec.
±0,025
Assembly Solenoid Armature
Assembly concept

## Slide 6
Danke
für die Aufmerksamkeit